## Slide 1: Microwatt Microarchitecture
Paul Mackerras
2024-Jul-30

## Slide 2: Introduction
Microwatt started as demo/proof-of-concept for announcement of Power ISA being made open (August 2019).
  Core structure is relatively simple
Code hosted on github, updated through pull requests
  Use automated testing to catch bugs early
Targets simulation and synthesis for FPGAs
  Artix-7, ECP5
Wishbone memory interface
Peripherals from Litex project
Aims to be a compliant PowerISA v3.1C implementation
  Includes support for prefixed instructions (2-word instructions)
Can run Linux

## Slide 3: Pipeline Overview
fetch1
icache
MMU
decode1
decode2
execute1
loadstore1/2
dcache
FPU
writeback
memory
memory
register_file
cr_file
execute2
PMU

## Slide 4: System overview
Core
Wishbone
arbiter
Address
decoder
L2C/
DRAM
BRAM
I/O decoder
SYSCON
SPI flash
UART
XICS
ENET
JTAG/
debug
SDcard

## Slide 5: Fetch1 and icache
Fetch1 generates a sequence of effective and corresponding real addresses
  Increment by 4 each cycle unless redirected by decode1 or writeback
    Branches, interrupts, rfid, isync cause redirects
  Contains instruction TLB and tiny 2-entry cache of TLB
  Contains (optional) Branch Target Cache (BTC)
    Stores instruction address, target address and taken indication for executed direct branches
Icache reads and caches instructions from memory
  Use of real address for index and tag avoids aliasing problems
  Instructions are predecoded into 36-bit form on icache refill
    6-bit primary opcode gets replaced by 10-bit instruction index determined from primary and extended opcodes
  No support currently from fetching from cache-disabled pages of memory
  Icache snoops writes to memory and invalidates corresponding lines

## Slide 6: Decode1 and decode2
Decode1 looks up a decode ROM using instruction index
  Decode ROM gives control signals used to control operand decoding, ALU function, result selection, etc.
  Does static branch prediction for direct branches
  Computes register file addresses (GPRs and FPRs) for up to 3 register operands
  Decodes SPR (special purpose register) numbers
Decode2 does instruction scheduling and dispatch
  Calculates instruction dependencies and stalls until operands are available
  Forwards operands from previous instruction results (where available)
  Does immediate operand selection and formatting
    Operand can come from instruction field, or be the address of the instruction
  Computes some control signals for execute stage

## Slide 7: Prefixed Instructions
lfd f2,0x20(r4)
2
4
50
plfd f2,0x123450020(r4),0
0x12345
2
0
1
260
2
4
After predecoding
Word instruction:
Prefixed instruction:
2
4
50
0x20
0x12345
2
0
2
2
4
260
260
After predecoding
Decode1 uses entry 260
Decode1 uses entry 261
0x20
0x20
0x20

## Slide 8: Execute1 and execute2
Executes all instructions except load/store and FPU instructions
  64-bit integer multiply and integer division are now done by FPU (if present)
Submodules handle shift/rotate instructions, logical instructions, count-bits instructions, 32-bit multiplications
“Main adder” performs add/subtract instructions
Exception detection and interrupt generation
Interlocks to ensure instructions complete in order
Execute1 does most integer computations and forwards results to decode2
  Count-bits, multiply, and some move from SPR instructions take 2 cycles to generate their result, so their results are not forwarded from execute1
Execute2 does updating of SPRs, condition-code result generation for dot-form instructions, and forwarding of results.

## Slide 9: Loadstore1/2 and dcache
Loadstore1 receives instruction from execute1
  Evaluates whether the access is misaligned and crosses a doubleword boundary
  Converts FP data to single-precision form for stfs[x] instruction
Effective address sent to dcache in first cycle
Dcache reads the cache RAM, cache tag, and TLB in the second cycle
  Dcache is store-through; all stores are written to memory immediately
  Cache tags and TLB looked up in parallel; both can have multiple ways
    Matrix of tag comparators to decide on TLB and cache hits
  State machine to handle stores, load misses and non-cacheable loads
  Store data forwarded to later loads to avoid stalling load-hit-store cases
For loads, formatting of result data occurs in third (writeback) cycle
  Except conversion of single-precision data to DP form (lfs[x]) takes an extra cycle
Loadstore 2 (and 3) has state machine to handle complex cases

## Slide 10: Memory management unit
ISA defines two address translation schemes
  Hashed page table (HPT), used by AIX and IBM/i and older Linux kernels
  Radix page table, used by recent Linux kernels
Microwatt implements radix and not HPT
ISA defines a very general tree structure for radix trees
PTCR
Partition table
Indexed by LPIDR
Process table
Indexed by PIDR
Radix page tables
Page
Indexed by address bitfields

## Slide 11: Memory management unit
Radix tree page directory entry format:
  NLS = Next level size, number of bits used to index next level of tree
Two standard layouts defined in ISA
  52-bit EA, 4 levels, 64k page size (index fields 13, 9, 9, 5 bits)
  52-bit EA, 4 levels, 4k page size (index fields 13, 9, 9, 9 bits)
Microwatt implements a general radix tree walker state machine
  Any NLS value from 5 to 16 is permitted
  Address space size from 31 bits (2 GiB) to 62 bits (4 EiB)
  Any power-of-2 page size >= 4 kiB
  Any number of levels between 1 and 10
L
V
NLB
NLS

## Slide 12: Memory management unit
Level-1 TLBs in fetch1 and dcache
  4kB page size, looked up in parallel with cache tags
  Instruction TLB is direct-mapped, 64 entries
  Data TLB is 2-way set associative, 128 entries total
MMU is a state machine
  Sends a series of requests to the dcache to read the process table and PTEs
  Eventually sends the translation to the dcache or fetch1
    EA bits inserted if page size > 4kB
Currently no caching of PTEs or PDEs in the MMU
  Nor any caching of partial translation results (no “page walk cache”)
  Just the L1 iTLB and dTLB inside the instruction and data caches
Microwatt implements vestigial (1 entry) partition table

## Slide 13: Floating-point unit
Non-pipelined
  Has its own data path with 64-bit adder, shifter, multiplier (64x64 → 128) and count-leading-zeroes logic
Control is a state machine
  Implemented with “random” logic (not microcode)
  One operation at a time
  Add/subtract generally take 5–12 cycles, multiply takes 8–15 cycles
Handles all architected exception conditions
  Denormalized operands and results
  Underflow and overflow conditions, including trap-enabled and trap-disabled results

## Slide 14: FPU – Data paths (simplified)
A
B
C
R
S
Shifter
Adder
Multiply/
add
P
Y
Lookup table
To writeback
Count zeroes
Shift
Constants